## Slide 1: Logic Gates
A gate is a device that performs a basic operation on electrical signals.
Gates are combined into circuits to perform more complicated tasks.

## Slide 2: Logic Gates
There are three different, but equally powerful, notational methods for describing the behavior of gates and circuits
  Boolean expressions
  logic diagrams
  truth tables

## Slide 3: Logic Gates
Boolean algebra: expressions in this algebraic notation are an elegant and powerful way to demonstrate the activity of electrical circuits

## Slide 4: Logic Gates
Logic diagram: a graphical representation of a circuit
  Each type of gate is represented by a specific graphical symbol
Truth table: defines the function of a gate by listing all possible input combinations that the gate could encounter, and the corresponding output.

## Slide 5: Gates
Types of gates
  NOT
  AND
  OR
  XOR
  NAND
  NOR
Typically, logic diagrams are black and white, and the gates are distinguished only by their shape

## Slide 6: NOT Gate
A NOT gate accepts one input value and produces one output value

## Slide 7: NOT Gate
By definition, if the input value for a NOT gate is 0, the output value is 1, and if the input value is 1, the output is 0
A NOT gate is sometimes referred to as an inverter because it inverts the input value

## Slide 8: AND Gate
An AND gate accepts two input signals
If the two input values for an AND gate are both 1, the output is 1; otherwise, the output is 0

## Slide 9: OR Gate
If the two input values are both 0, the output value is 0; otherwise, the output is 1

## Slide 10: XOR Gate
XOR, or exclusive OR, gate
  An XOR gate produces 0 if its two inputs are the same, and a 1 otherwise
  Note the difference between the XOR gate and the OR gate; they differ only in one input situation
  When both input signals are 1, the OR gate produces a 1 and the XOR produces a 0

## Slide 11: XOR Gate

## Slide 12: NAND and NOR Gates
The NAND and NOR gates are essentially the opposite of the AND and OR gates, respectively

## Slide 13: Review of Gate Processing
A NOT gate inverts its single input value
An AND gate produces 1 if both input values are 1
An OR gate produces 1 if one or the other or both input values are 1

## Slide 14: Review of Gate Processing (cont.)
An XOR gate produces 1 if one or the other (but not both) input values are 1
A NAND gate produces the opposite results of an AND gate
A NOR gate produces the opposite results of an OR gate

## Slide 15: Gates with More Inputs
Gates can be designed to accept three or more input values
A three-input AND gate, for example, produces an output of 1 only if all input values are 1

## Slide 16: Types of Logic Gates

## Slide 17: DeMorgan’s Theorems
DeMorgan’s Theorems are two additional simplification techniques that can be used to simplify Boolean expressions. Again, the simpler the Boolean expression, the simpler the resulting logic.
Notes: Introductory Slide / Overview of Presentation

## Slide 18: DeMorgan’s Theorem #1
0 | 0 | 0 | 1
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 1 | 0 | 0 | 0
Proof
The truth-tables are equal; therefore, the Boolean equations must be equal.
Notes: Overview & proof of DeMorgan’s Theorem #1

## Slide 19: DeMorgan’s Theorem #2
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0
Proof
The truth-tables are equal; therefore, the Boolean equations must be equal.
Notes: Overview & proof of DeMorgan’s Theorem #2

## Slide 20: Boolean Equations
All Boolean Equations are written in one of two formats:
• SOP (Sum of Products) – (AND) OR (AND) OR … OR (AND)
• POS (Product of Sums ) – (OR) AND (OR) AND … AND (OR)

## Slide 21: Boolean Equations
Use Boolean Theorems and Postulates, DeMorgan’s Theorem, or the Karnaugh Map to reduce the number of gates
– Decreases cost
– Increases reliability

## Slide 22: Boolean Laws
OR Identities AND Identities
A + 0 = A A * 0 = 0
A + 1 = 1 A * 1 = A
A + A = A A * A = 0
A + A = 1 A * A = A

## Slide 25: De-Morgan’s Theorem and Logic Conversion
1)
2)
3)
4)

## Slide 26: Implement the logic expression using NAND gates only
1)
2)

## Slide 27: Implement logic expression using NOR gates only
1)